## Slide 1: Project Description
Performing Kinesthetic Motor Imagery (MI)
What happens to the brain activity (record from 16 electrodes-cap)?
Beta rebound could be used to decode when the use wants to stop motor imagery
Why studying Kinesthetic MI?
ERS mu
ERS mu
ERD beta
ERD mu
ERS beta (beta rebound)
Beta band=18-30 Hz
Mu band=8-12 Hz
Notes: It has been observed that preceding movement onset and during movement execution, a decrease of power can be detected in mu band (8-12 Hz) as well as an increase of power in beta band (13-30 Hz), called beta rebound, over the contralateral sensorimotor cortex.

## Slide 2: Protocol
START
END
Beta rebound
4 runs (cue-based) of 30 trials of 10 sec plus 7 sec of relax each.
Notes: Changes in the brain rhythms are observed in the sensory-motor area of brain during planning and execution of movements. Indeed, it has been observed that preceding movement onset and during movement execution, a decrease of power can be detected in mu band (8-12 Hz) as well as in beta band (13-30 Hz) over the contralateral sensorimotor cortex (Pfurtscheller & Lopes Da Silva, 1999). Additionally, the beta band presents an increase of power known as the beta rebound, which generally occurs after movement termination and that can last for a second (Thatcher, Sato, Kufta, & Hallett, 1994). This beta rebound does not necessarily depend on motor cortex output and muscle activation since this beta rebound has been also reported in motor imagery (MI) and it is thought to reflect a short-lasting state of deactivation or inhibition of motor cortex networks

## Slide 3: EEG correlates - Methods

## Slide 4: EEG correlates - Methods
Concatenation of all runs for each subject
Comparison of two different spatial filters: Laplacian filter and CAR filter
Epoching of the data based on the event type and the chosen time before and after the selected event
  Baseline (-3; 3)
  Motor Imagery initiation (-4; 2)
  Motor Imagery termination (-3; 3)
Pwelch on car data to obtain the periodogram to compare baseline and Motor Imagery
  win=512, noverlap=0.5*512, frequency=500 Hz, sample rate=512 Hz
Spectrogram on the most relevant channels
Grand average over the three subjects
Topoplots in alpha band (8-12 Hz) and beta band (13-30 Hz) for both onset and offset, using the a 2 seconds window (-1:0.25:+1) with respect to the event alignment

## Slide 5: EEG correlates - Results

## Slide 6: Spectrogram offset and onset CAR - ak4
The presence of the beta rebound is clearly visible for C1, C3 and CP4 but a sort of “alpha rebound” is also present at lower frequencies

## Slide 7
As expected, the beta rebound is particularly visible with the offset boundaries.
Grand average over all three students - CAR (offset)

## Slide 8: Grand average over all three students - CAR (onset)
All the important events (ERD in blue and ERS in red) are visible in all the grand averaged plots, in both cases of onset and offset.

## Slide 9
Spectrogram using the laplacian spatial filter. Comparing it to the same graphs obtained with the CAR filter, it is evident how this last one allows a better understanding of the interested phenomenon in all the channels. Therefore, CAR has been chosen for further analysis.
Spectrogram offset and onset Laplacian - ak4

## Slide 10: Periodogram (Pwelch) offset/onset ak6
The periodogram shows the PSD depending on the frequency. We only showed the region of interest until 50 Hz. The presence of two bumps in the alpha band can be seen in the most relevant channels when comparing baseline and MI

## Slide 11: Periodogram (Pwelch) offset/onset ak4

## Slide 12: Periodogram (Pwelch) offset/onset ak5

## Slide 13: Topoplot alpha band - ak6

## Slide 14: Topoplot alpha band - ak4
Topolot in the mu band (8-12 Hz) showing the activation of different regions aligned with a specific event. A decrease in the alpha band can be seen after the onset alignment and during the motor imagery. Moreover, a considerable increase is visible after the MI termination, during the relax phase

## Slide 15: Topoplot alpha band - ak5

## Slide 16: Topoplot beta band - ak6

## Slide 17: Topoplot beta band - ak4
Topoplot in the beta band (13-30 Hz). The presence of the beta rebound is very evident after the MI termination while lower power is visible during the MI initiation

## Slide 18: Topoplot beta band - ak5

## Slide 19: Pattern Classification - Methods

## Slide 20: Pattern Classification - Methods
4 runs (4∙30=120 trials) per subject
Spatial filtering: CAR. Temporal filtering: None.
Performed spectrogram on the whole signal (for each run)
  4:2:40 Hz =>19 intervals
  16 channels
Divided the signal into 1 second long windows with a shift of 0.0625 s
Epoching on :
  Motor Imagery Initiation => Event ID: 555 [ -2,0 ] (sec) => Manually (re)assigned label 400
  Motor Imagery Termination => Event ID: 555 [0.5,2.5] (sec)
=> We obtained 17 windows for each trial for each type of event (i.e. 17 ∙ 2 = 34)
We concatenated the runs
=> 120 ∙ 34 = 4080 samples with 304 features
Classifier had to distinguish between two classes: ERD (MI initation) and ERS (MI Termination)
=> 304 different features (PSD)

## Slide 21: Methods Classifier
Divided into 70% training - 30% testing
CV on training but with temporal…. partition
  Normalization with zscore on training folds and “projection” on validation folds
We tried PCA but didn’t get good results
Hyperparameters:
  Type of classifier (linear, diaglinear, diagquadratic)
  Number of features (we tried from 1 to 304 but in the end chose among 1:20)
  (Number of PCs => 0)
=> Feature selection with Fisher’s score
=> Hyperparameter selection based on class error (of course on validation fold!) averaged over folds

## Slide 22: Methods Classifier
How to evaluate the capability?
=> Retraining on the whole training+validation set (but without CV), with the hyperparameters found before
For features: only the number of features is fixed, but of course which are the actual features to take is determined by retraining
=> Test on the separate 30% test set
Metrics:
- ROC curve
- confusion matrix
- class error

## Slide 23: Pattern Classification - Results

## Slide 24: Pattern Classification - Results
“Qualitative” Fisher’s score averaged over folds
Class error/ Confusion Matrix

## Slide 25: Discussion

## Slide 26
Thank you for your attention!
Any questions?

## Slide 27: Additional results

## Slide 28: Spectrogram offset and onset CAR - ak5

## Slide 29: Spectrogram offset (left) and onset (right) CAR - ak6

## Slide 30: Spectrogram offset and onset Laplacian - ak5

## Slide 31: Spectrogram offset and onset Laplacian - ak6